## Slide 1
AREA II:
LAND AND WATER RESOURCES ENGINEERING
Prepared by: Engr. Nicole Jane J. Lim
ABELE | 2025
ATTRC - Iligan City

## Slide 2
IRRIGATION AND DRAINAGE ENGINEERING
Surveying
Fluid Mechanics
Groundwater Hydrology
Pumps
Open Channel
Pressurized Irrigation Systems

## Slide 3
IRRIGATION AND DRAINAGE ENGINEERING
Groundwater Hydrology
Pumps
Open Channel
Pressurized Irrigation Systems
Fluid Mechanics
Surveying

## Slide 4
Groundwater Hydrology
Pumps
Open Channel
Pressurized Irrigation Systems
Surveying
FLUID MECHANICS

## Slide 5
QUESTION 1
This property is defined as a measure of a fluid's resistance to flow, and describes the internal friction of a moving fluid.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://chem.libretexts.org/Courses/University_of_Arkansas_Little_Rock/Chem_1402%3A_General_Chemistry_1_(Kattoum)
Shear rate
Viscosity
Consistency
Density

## Slide 6
Some Properties of Fluid Relevant in ABE
Reference: http://ecoursesonline.iasri.res.in/mod/resource/view.php?id=147003
Density - determines the mass of a fluid per unit volume and affects flow rates, buoyancy, and energy requirements in pumping systems. In irrigation, knowing the density helps calculate the force needed to move water through pipes and canals. It also affects the design of fluid storage and distribution systems.
Specific Gravity - this dimensionless property is the ratio of a fluid's density to that of water (reference density). Specific gravity helps in comparing different fluids in applications such as liquid fertilizers or pesticides, where the fluid's behavior under different conditions affects distribution.
Compressibility: Compressibility refers to the change in fluid volume under pressure. In ABE, most liquids are considered incompressible for ease of calculations. However, understanding compressibility is critical in systems where gases are involved, such as in pneumatic systems or air-assisted spraying, as it influences the system's efficiency and energy consumption.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 7
Some Properties of Fluid Relevant in ABE
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: http://ecoursesonline.iasri.res.in/mod/resource/view.php?id=147003
Capillarity: This property is the ability of a fluid to move through small spaces due to adhesive and cohesive forces. Capillary action is significant in soil moisture movement, affecting water availability to plants. It is also crucial in designing irrigation systems, particularly drip irrigation, where the controlled release of water relies on capillary action to spread moisture uniformly around roots.
Surface Tension: Surface tension affects the behavior of liquids at the interface with other materials. In agricultural spraying, surface tension impacts droplet formation, spread, and adhesion on plant surfaces, which are essential for effective pesticide or nutrient application. In micro-irrigation, controlling surface tension helps improve water distribution and minimize evaporation losses.
Pressure - pressure in fluids is determined by depth, density, and gravity. Understanding pressure is critical in designing water delivery systems, such as pumps and pipes, where sufficient pressure must be maintained to transport water efficiently. In irrigation, managing pressure ensures even water distribution, reducing energy costs and optimizing water use.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 8
QUESTION 2
Hydrometer is an instrument used to determine what characteristic of fluid?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Humidity
Flow rate
Velocity
Specific gravity
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 9
Some Fluid Mechanics Measuring Instruments
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://www.laboratorydeal.com/blogs/blogs/fluid-mechanics-physics-instruments-equipment
A hydrometer measures the density (specific gravity) of liquids, while a hygrometer measures the humidity (water vapor in the air).
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 10
QUESTION 3
Which of the following concepts derives its principle from the law of conservation of energy?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Darcy’s equation
Manning’s equation
Bernoulli’s equation
Hagen-Poisceuille equation
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 11
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 12
Darcy’s, Manning’s, Bernoulli’s, and Hagen-Poiseuille Equation and their Application in ABE
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Take note: Darcy’s law is only applicable for laminar flow. It defines the flow of a fluid through a porous medium
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 13
QUESTION 4
This is a dimensionless number that gives a measure of the ratio of inertial forces to viscous forces and, consequently, it quantifies the relative importance of these two types of forces for
given flow conditions.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://chem.libretexts.org/Courses/University_of_Arkansas_Little_Rock/Chem_1402%3A_General_Chemistry_1_(Kattoum)
Reynolds Number
Prandtl Number
Nusselt Number
Avogadro's Number
- represents the ratio of inertial to viscous forces within a fluid
- relates the viscosity of a fluid to its thermal conductivity
- ratio of convective heat transfer to conductive heat transfer in a fluid system
- number of units in one mole of any substance
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 14
QUESTION 5
Reynold’s number for laminar flow is?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://chem.libretexts.org/Courses/University_of_Arkansas_Little_Rock/Chem_1402%3A_General_Chemistry_1_(Kattoum)
Re < 2000
2000 < Re < 4000
Re > 4000
Re = 0
Laminar flow
Transitional flow
Turbulent flow
-----------------
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 15
QUESTION 6
This type of flow is one in which all conditions at any point in a stream remain constant with respect to time.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://learn.lboro.ac.uk/pluginfile.php/504741/mod_resource/content/1/Fluid_Mechanics_3.pdf
Uniform flow
Non-uniform flow
Steady flow
Unsteady flow
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 16
QUESTION 7
If the flow velocity is the same magnitude and direction at every point in the fluid, it is said to be in this type of flow.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://learn.lboro.ac.uk/pluginfile.php/504741/mod_resource/content/1/Fluid_Mechanics_3.pdf
Uniform flow
Non-uniform flow
Steady flow
Unsteady flow
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 17
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics
Uniform flow
Flow velocity is the same magnitude and direction at all points
Point A = Point B = Point C = …
Steady flow
This type of flow is one in which all conditions at any point in a stream remain constant with respect to time.
Point A @ T1 = Point A @ T2 = …
Point B @ T1 = Point B @ T2 = …

## Slide 18
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://learn.lboro.ac.uk/pluginfile.php/504741/mod_resource/content/1/Fluid_Mechanics_3.pdf
Uniform flow
The conditions (velocity, pressure and cross-section) may differ from point to point but do not change with time.
The velocity is not the same at every point.
Non-uniform flow
Steady flow
Unsteady flow
The flow velocity is the same magnitude and direction at every point in the fluid.
The conditions change with time.
Uniform flow
Non-uniform flow
Unsteady flow
In practice there is always slight variations in velocity and pressure, but if the average values are constant, the flow is considered steady.
Steady flow
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 19
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://learn.lboro.ac.uk/pluginfile.php/504741/mod_resource/content/1/Fluid_Mechanics_3.pdf
Uniform flow
The conditions (velocity, pressure and cross-section) may differ from point to point but do not change with time.
The velocity is not the same at every point.
Non-uniform flow
Steady flow
Unsteady flow
The flow velocity is the same magnitude and direction at every point in the fluid.
The conditions change with time.
Uniform flow
Non-uniform flow
Unsteady flow
Steady flow
Steady uniform flow
Steady non-uniform flow
Unsteady uniform flow
Unsteady non-uniform flow
Conditions do not change with position in the stream or with
time.
Conditions change from point to point in the stream but
do not change with time.
At a given instant in time the conditions at every point are
the same, but will change with time.
Every condition of the flow may change from point to
point and with time at every point.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 20
ADDITIONAL QUESTION
What type of flow does a water flowing at a constant rate through a conical pipe exhibit, based on the previous discussion?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://chem.libretexts.org/Courses/University_of_Arkansas_Little_Rock/Chem_1402%3A_General_Chemistry_1_(Kattoum)
Water flowing at a constant rate through a conical pipe exhibits steady, non-uniform flow.
Why steady?
The flow rate is constant over time.
This means that at any fixed point in the pipe, the velocity, pressure, and other properties do not change with time.
Why non-uniform?
The cross-sectional area of a conical pipe changes (either narrowing or widening).
So the velocity changes from point to point along the pipe due to continuity (as area decreases, velocity increases, and vice versa).
Hence, flow properties vary with position, making it non-uniform in space.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 21
QUESTION 8
A hydraulic jump is an example of which type of flow?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://chem.libretexts.org/Courses/University_of_Arkansas_Little_Rock/Chem_1402%3A_General_Chemistry_1_(Kattoum)
Laminar
Turbulent
Gradually varied flow
Rapidly varied flow
Rapidly-varied flow is a significant change in water depth over a short distance. Gradually Varied Flow (GVF) is the flow where the water depth changes gradually over a large distance and usually connects RVF and UF.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 22
QUESTION 8
This dimensionless number which represents the ratio of inertial and gravitational forces value and describes different flow regimes of open channel flow.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Reynold’s number
Froude’s number
Weber's number
Euler's number
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 23
QUESTION 9
What is the rate of flow of coconut oil in a 2 in. pipe if the velocity of the fluid is measured at 0.02 m/s? The specific weight of oil is 1500 kg/cubic meter?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
0.01lps
0.02lps
0.03lps
0.04lps
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 24
QUESTION 9
What is the rate of flow of coconut oil in a 2 in. pipe if the velocity of the fluid is measured at 0.02 m/s? The specific weight of oil is 1500 kg/cubic meter?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
0.01lps
0.02lps
0.03lps
0.04lps
Solution:
Q = 0.00004054m3/s or 0.04lps
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 25
QUESTION 10
The U-shaped tube as shown contains mercury that has a density of 13‎ ‎595 kg/m3. The top of the mercury column in contact with the atmosphere is vertically below the top of the mercury column in contact with the gas reservoir. The vertical distance between the column tops h = 25cm. Find the pressure of the gas in the reservoir.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
33kPa
68kPa
101kPa
105kPa
Reference: https://www.nagwa.com/en/explainers/216152184514/
-----------
-----------
Liquid Manometer Equation: ΔP = ρgΔh
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 26
Recall: Pressure measurement using the height of a liquid column in a U-shaped manometer
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
Reference: https://www.nagwa.com/en/explainers/216152184514/
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics
Notes: 2nd image Patm – Pgas = "ρg∆h" therefore Pgas = Patm - "ρg∆h"
3rd image Pgas – Patm = "ρg∆h" therefore Pgas = Patm = "ρg∆h"

## Slide 27
QUESTION 10
The U-shaped tube as shown contains mercury that has a density of 13‎ ‎595 kg/m3.The top of the mercury column in contact with the atmosphere is vertically below the top of the mercury column in contact with the gas reservoir. The vertical distance between the column tops h = 25cm. Find the pressure of the gas in the reservoir.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
33kPa
68kPa
101kPa
105kPa
Reference: https://www.nagwa.com/en/explainers/216152184514/
Solution:
Pg = Patm - ρgΔh
Pg = 101.3kPa – (13595kg/m3)(9.81m/s2)(0.25m)
Pg = 67.95kPa
-----------
-----------
Liquid Manometer Equation: ΔP = ρgΔh
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 28
QUESTION 11
The pressures of the gas reservoirs are P = 110.3kPa and P = 110.1kPa.The U-shaped tube contains an oil with a density of 1‎ ‎080 kg/m3. What is the vertical distance h between the tops of the oil columns?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
2.54cm
2.25cm
1.92cm
1.89cm
Reference: https://www.nagwa.com/en/explainers/216152184514/
Liquid Manometer Equation: ΔP = ρgΔh
Solution:
ΔP = ρgΔh
(110.3kPa – 110.1kPa) x 1000Pa/kPa = (1080kg/m3)(9.81m/s2) Δh
Δh = 0.0189m or 1.89cm
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 29
QUESTION 11
Using Bernoulli’s equation, find the velocity at the end of a pipe given the following conditions:
V = 0.8m/s
P1 = 15kPa
P2 = 13kPa
Density = 1.2g/cc
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
1.66m/s
1.77m/s
1.88m/s
1.99m/s
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Solution:
Using shift solve:
v2 = 1.99m/s
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 30
QUESTION 12
What must be the drop of height of a pipe in order to achieve a pressure of 2.5atm if the initial pressure is set at atmospheric value? Assume that the fluid velocity is constant with a density of 1100kg/m3.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
-14.09m
-18.2m
-16.57m
-14.33m
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Solution:
Since velocity is constant:
This can be re-written as:
-14.09m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 31
QUESTION 13
A horizontal fully flowing, 4-inch pipe is discharging water. The X-coordinate and Y-coordinate of the water trajectory as measured from the end of the pipe are 1.5 m and 0.8 m, respectively. Assuming that the coefficient of discharge is 1.0. What is the discharge of the pipe?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
8.34lps
30.03lps
132.23lps
476.04lps
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Formula for hydraulic jump:
Q = 3.6
Where: Q = GPM
A = in2
X and Y = in
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 32
QUESTION 13
A horizontal fully flowing, 4-inch pipe is discharging water. The X-coordinate and Y-coordinate of the water trajectory as measured from the end of the pipe are 1.5 m and 0.8 m, respectively. Assuming that the coefficient of discharge is 1.0. What is the discharge of the pipe?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Fluid Mechanics
8.34lps
30.03lps
132.23lps
476.04lps
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Solution (Belonio formula):
Q = 3.6 where Q = gpm, rest is inches
Q = 3.6 x
Q = 476.04gpm x
Q = 30.03lps
Alternative solution:
Q = CdA where h = x – y Q = m3/s, rest is meters
Q = (1.0)
Q = 0.03004m3/s or 30.04lps
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Fluid Mechanics

## Slide 33
THANK YOU
ABELE | 2025
ATTRC - Iligan City