## Slide 1
AREA II:
LAND AND WATER RESOURCES ENGINEERING
Prepared by: Engr. Nicole Jane J. Lim
ABELE | 2025
ATTRC - Iligan City

## Slide 2
IRRIGATION AND DRAINAGE ENGINEERING
Surveying
Fluid Mechanics
Groundwater Hydrology
Pumps
Open Channel
Pressurized Irrigation Systems

## Slide 3
IRRIGATION AND DRAINAGE ENGINEERING
Surveying
Fluid Mechanics
Groundwater Hydrology
Pumps
Open Channel
Pressurized Irrigation Systems

## Slide 4
Surveying
Fluid Mechanics
Groundwater Hydrology
Pumps
Pressurized Irrigation Systems
OPEN CHANNEL

## Slide 5
IRRIGATION WATER REQUIREMENT AND RELATED FORMULAS
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Reference: PAES 602:2016
Land preparation water requirement (LPWR) - amount of water required in lowland rice production which includes water losses through evaporation, seepage and percolation and land soaking
LPWR = LSR + SW + ETo
Land soaking water requirement (LSR) - amount of water required in lowland rice production which is a function of the initial soil moisture and the physical properties of the soil
LSR =

## Slide 6
IRRIGATION WATER REQUIREMENT AND RELATED FORMULAS
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: PAES 602:2016
Farm Irrigation Requirement – farm water requirement minus the application losses
FIR =
Diversion Requirement – farm water requirement plus conveyance losess
DR =
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 7
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
Depth of Irrigation
Based on field capacity and available moisture prior to irrigation
d =
Irrigation Interval
II =
where: FC = field capacity
AM = available moisture prior to irrigation
D = depth of rootzone
Ea = application efficiency
p = fraction of available soil water that permits unrestricted ET
ET = evapotranspiration
ER = effective rainfall
IRRIGATION APPLICATION AND SCHEDULING
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 8
IRRIGATION EFFICIENCY
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
Water conveyance efficiency – ratio of water delivered to water diverted
Water application efficiency – ratio of water stored in the root zone to water delivered to the farm
Water-use efficiency – ratio of water beneficially used to water delivered
Water storage efficiency – ratio of water stored in the root zone during irrigation to water needed in the root zone prior to irrigation
Consumptive use efficiency – ratio of normal consumptive use to the net amount of water depleted from root zone
Water distribution efficiency – ratio of the average numerical deviation in depth stored during irrigation to the average depth of water stored during irrigation
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 9
TIP
UNDERSTANDING
RATHER THAN
MEMORIZING

## Slide 10
QUESTION
Twelve thousand two hundred fifty cubic meters of water was delivered to a 10-ha farm for the month of June in which consumptive use is estimated at 8mm/day. The effective rainfall for the period was 150mm. What is the irrigation efficiency?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 73%
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: IE = [(CU x 30 days) – ER]/water delivered

## Slide 11
QUESTION
Evapotranspiration in an 8 ha farm is 7 mm/day and percolation losses is 2 mm/day. What is the design discharge of a canal to be able to deliver a 5-day requirement of the farm in 24 hours if irrigation efficiency is 75%?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 200m3/hr
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: Q = [(ET + P) x 5 days x 8 x 10000]/24h x 0.75

## Slide 12
QUESTION
Determine the irrigation interval for a farm with soil root zone having a field capacity of 200 mm and a wilting point of 105 mm. Assume that the consumptive use for August is 7.5 mm/day with no rainfall and the allowable moisture depletion is 75%.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 9 days
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: II = [(FC-PWP) x MAD]/CU

## Slide 13
QUESTION
What is the design discharge of a canal to be able to deliver 7-day requirement of a 5-ha farm in 12 hours if the irrigation requirement is 8mm/day?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 233.33m3/hr or 0.065m3/s
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 14
QUESTION
Compute the land soaking requirement for a soil (depth of root zone = 60 cm) with residual moisture content of 18% by weight, bulk density of 1,320 kg/m³ and porosity of 50%. Standing water for planting is 20 mm.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 157.44mm
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 15
QUESTION
What is the root zone depth of a farm with land soaking requirement of 90 mm if the soil porosity is 45%, residual moisture content is 18% (by weight) and bulk density is 1,250 kg/m³?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. 400mm
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 16
QUESTION
In a 5 ha area, it was determined that the soil volumetric field capacity and permanent wilting point are 25% and 15%, respectively. Crop consumptive use is 5 mm/day, application efficiency is 80% and irrigation application rate is 60 m³/hr. The allowable soil moisture depletion is 60%, apparent specific gravity is 1.2 and the depth of root zone is 0.8 m. Determine the following: a) dnet b) dgross
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. a) 48mm
b) 60mm
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 17
QUESTION
In a 5 ha area, it was determined that the soil volumetric field capacity and permanent wilting point are 25% and 15%, respectively. Crop consumptive use is 5 mm/day, application efficiency is 80% and irrigation application rate is 60 m³/hr. The allowable soil moisture depletion is 60%, apparent specific gravity is 1.2 and the depth of root zone is 0.8 m. Determine the following: c) irrigation interval d) irrigation period
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans. c) 9 days
d) 50 hours
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 18
QUESTION
Surface irrigation method where a much smaller area is enclosed by levees
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Border strip irrigation
Basin flooding
Trickle irrigation
Furrow irrigation
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 19
IRRIGATION METHODS
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
Surface Irrigation Method
Sprinkler Irrigation Method
Sub irrigation ang Drip Irrigation Method
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 20
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.fao.org/4/t0231e/t0231e04.htm
Surface Irrigation Methods
Basin irrigation - most common form of surface irrigation, particularly in regions with layouts of small fields. If a field is level in all directions, is encompassed by a dyke to prevent runoff, and provides an undirected flow of water onto the field, it is herein called a basin.
Border strip irrigation - water is applied to individual borders from small hand-dug checks from the field head ditch. When the water is shut off, it recedes from the upper end to the lower end.
Furrow irrigation - widely used for irrigation of row crops. Corrugations or small furrows are simply narrow ditch between rows of crops with about 0.2 to 0.5 of surface area wetted during irrigation. Water infiltrates through the wetted perimeter and spreads vertically and horizontally to refill the soil reservoir.
IRRIGATION METHODS
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 21
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: PAES 607:2016
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 22
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
3. Sub irrigation and Drip irrigation Method
Sub irrigation – applying water to the soil directly under the ground surface
Drip irrigation – also trickle irrigation. Allows frequent or slow application of water either directly on land surface or into the root zones of crops
Drip or trickle irrigation is considered the most efficient irrigation method.
IRRIGATION METHODS
2. Sprinkler irrigation – application of water in the form of spray over the land
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 23
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
The water is directed to the base of the plant. Water is applied to the soil through small orifices .
The surface is rarely wet since the water is supplied from the soil underneath. This requires complete control of the water table so that the root zone is kept relatively free of excess water but is continually supplied with capillary moisture during the cropping season.
It is accomplished by running water through small channels or furrows while it moves down or across the slope of the field.
QUESTION
Furrow irrigation
Sub irrigation
Drip/trickle irrigation
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 24
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
CONVEYANCE, DISTRIBUTION AND MANAGEMENT STRUCTURES
Headwork structures
Conveyance structures
Control structures
Protective structures
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 25
QUESTION
It refers to the composite parts of the irrigation system that divert water from natural bodies of water such as rivers, streams and lakes.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.bfar.da.gov.ph/wp-content/uploads/2021/03/Republic-Act-8435.pdf
Headworks
Diversion canal
Channel
Headgate
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 26
QUESTION
This refers to a closed conduit designed to convey canal water in full and other pressure running condition, to convey canal water by gravity under roadways , railways, drainage channels and local depressions.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Siphon
Inverted siphon
Flume
Culvert
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 27
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Division box

## Slide 28
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 29
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 30
QUESTION
Which of the following best describes how flow rate is related to velocity?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.valin.com/resources/blog/introduction-pressure-part-ii-velocity-flow-rate-and-reaction-force
The volumetric flow rate is directly proportional to the velocity of the flowing fluid passing through a given cross sectional area.
The flow rate decreases as the velocity of the fluid increases in a constant cross-sectional area.
The flow rate is inversely proportional to the velocity of the fluid in a constant cross-sectional area.
The flow rate remains constant regardless of changes in the fluid velocity and cross-sectional area.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 31
QUESTION
Given an irrigation depth of 30 cm and 10 hours of irrigation time, determine the discharge needed to irrigate a hectare of land.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Ans.: 300m3/hr
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 32
QUESTION
All of the following can be used to measure the velocity of flowing liquid, except?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Manning’s Equation
Float Method
Current Meter Method
Hydrometer method
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 33
METHODS OF VELOCITY MEASUREMENT
Velocity by Float Method
Q = AV Vs = V = 0.8Vs
Velocity by Current Meter Method
V = a + bN
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
where: a = starting velocity
b = proportionality constant
N = speed of impeller
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 34
METHODS OF VELOCITY MEASUREMENT
Velocity by Float Method
Q = AV Vs = V = 0.8Vs
Velocity by Current Meter Method
V = a + bN
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
where: a = starting velocity
b = proportionality constant
N = speed of impeller
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 35
METHODS OF VELOCITY MEASUREMENT
Velocity by Current Meter Method
V = a + bN
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 36
QUESTION
Using the float method in determining the velocity of water in a channel, the float velocity in relation to the average water velocity is ____.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Equal to average water velocity
Less than to average water velocity
Greater than average water velocity
No relation at all
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 37
QUESTION
The velocities at 0.2 and 0.8 of the depth of flow in a 1.0 m wide rectangular open channel are 1.2 m/s and 0.3 m/s respectively. If the flow depth is 0.8m, the discharge is?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Ans.: 0.6m3/s
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 38
METHODS OF VELOCITY MEASUREMENT
Parshall Flume
Measures flow by noting the head loss caused by forcing a stream of water through a throat or constricted section of the flume with a depressed bottom.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 39
Velocity by Orifice Opening
V = where: h = depth of water (cm) above opening
Q = CdAV where: Cd value ranges from 0.027 to 0.035, depending on the position of orifice
Sharp Crested Weirs
Rectangular weir (Francis weir) Q = 0.0184LH3/2
Rectangular weir with contraction Q = 0.0184(L – 0.2H)H3/2
Trapezoidal weir (Cipoletti weir) Q = 0.0186LH3/2
900 triangular weir Q = 0.0138H5/2
Where: Q = discharge (lps)
L = width of weir (cm)
H = total head (cm)
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 40
WEIRS
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Q = CLHm
Where: Q – discharge
C – coefficient, dependent on the nature of the crest and approach conditions.
L – length of crest
H – head of the crest
m – exponent, depending upon the weir opening
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: A weir is a barrier across the width of a river that alters the flow characteristics of water and usually results in a change in the height of the river level. They are also used to control the flow of water for outlets of lakes, ponds, and reservoirs.
A weir is a notch of regular form through which the water/irrigation stream is made to flow. The notch may be rectangular, trapezoidal, or triangular.
In the context of weirs, contractions refer to restrictions in the flow width, either due to the geometry of the weir opening or the channel. End contraction occurs when the weir does not span the full width of the channel, resulting in a smaller effective flow width. Contractions impact the flow rate by changing how water accelerates as it approaches the weir, which is crucial for accurate discharge calculations.

## Slide 41
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Where: Q = discharge (cfs)
L = width of weir (f)
H = total head (f)
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 42
QUESTION
The theoretical flow velocity in an orifice is 4 m/s, what is the height of water flowing the center of the orifice?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Ans.: 0.82m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: V = sqr 2gh

## Slide 43
QUESTION
A rectangular lined canal will be used to irrigate 60 has. If a Francis weir of 0.4m crest will be used to control the flow, what would be the depth of water over the crest in order to supply 2 lps/ha?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Answers: h = 0.30m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: Q = 0.0184LH3/2

## Slide 44
QUESTION
If the canal in the previous condition is changed into a triangular canal, what would be the depth of water over the crest if a V-notch weir is used?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Answers: h = 0.38m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Notes: Q = 0.0138H5/2

## Slide 45
QUESTION
What is the depth of water flowing on a 900 V-notch weir if the water cross-sectional area is 0.5 m2?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Answers: y = 0.71m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 46
MANNING’S VELOCITY EQUATION
V = where: k = 1 for SI units, 1.486 for English units
n = roughness coefficient
R = hydraulic radius (m, ft)
s = slope gradient
Q =
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 47
Open Channel Flow
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
An open channel is a waterway, canal or conduit in which a liquid flows with a free surface. It describes the
flow in rivers, man-made channels and partially-full pipes (sewers, drains), as well as the
behavior of hydraulic structures such as weirs, spillways and sluices.
Open channel is considered the most common method of conveying water for the irrigation.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 48
QUESTION
This refers to a channel built with unvarying cross-section and constant bottom slope.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.usgs.gov/faqs/what-groundwater
Open channel
Open conduits
Prismatic channel
Non-prismatic channel
- the cross-section is non-uniform or the bottom slope is not constant. Natural
channels are usually non-prismatic channel.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 49
QUESTION
When the water level in the pipe drops below the upper edge of the pipe or culvert and its conduit controls, the flow becomes:
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Open channel
Open conduits
Prismatic channel
Non-prismatic channel
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 50
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
RECALL
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 51
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
RECALL
The most simple form of open channel flow computation.
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 52
FROUDE NUMBER
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Froude number is a dimensionless value that describes different flow regimes of open channel flow. The Froude number is a ratio of inertial and gravitational forces.
F =
When F = 1, the flow is said to be in critical state. The equation becomes:
V =
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 53
OPEN CHANNEL HYDRAULICS
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Geometric elements for channel cross sections
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 54
Important Terminologies
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.sciencedirect.com/book/9780750659789/hydraulics-of-open-channel-flow
Channel section refers to the cross section of a channel taken normal to the direction of flow.
Depth of flow, y is the vertical distance of the lowest point of a channel section from the free surface (or depth of flow section, d)
Stage is the elevation or vertical distance of the free surface above a datum. If the lowest point of the channel section is chosen as the datum, the stage is identical with the depth of flow.
Top width, T is the width of channel section at the free surface.
Water area, A - is the cross-sectional area of the flow normal to the direction of flow.
Wetted perimeter, P is the length of the line of intersection of the channel wetted surface with a cross-sectional plane normal to the direction of flow.
Hydraulic radius, R is the ratio of the cross sectional area to the wetted perimeter
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 55
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 56
OPEN CHANNEL HYDRAULICS
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Best hydraulic section
half of a perfect hexagon
half of a square
half of a square
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 57
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Reference: https://www.fsl.orst.edu/geowater/FX3/help/8_Hydraulic_Reference/Froude_Number_and_Flow_States.htm
Critical Flow In Open Channels
When the flow is at critical depth, the Froude number is equal to 1. This gives the following equality below, relating the area and top width of flow to the discharge of the channel and gravity.
SPECIFIC ENERGY AND CRITICAL FLOW
A = area (m2, ft2)
T = top width (m, ft)
Q = discharge (m3/s, cfs)
g = gravity (9.81m/s2, 32.2fps)
Specific energy is the sum of the depth of flow and the velocity head. Specific energy at a cross-section is:
If yactual > ycritical, flow is subcritical
If yactual < ycritical, flow is supercritical
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel

## Slide 58
QUESTION
What is the depth of water in a trapezoidal channel with a side slope of 2 and carrying a 2.5 m3/s water flow? The channel’s bottom width is 1.5 meters and the flowing water has a velocity of 0.8 m/s.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Ans.: 0.93m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Q = AV
A = = = 3.125m2
3.125 = (b + mh)h
3.125 = (1.5 + 2h)h
By shift solve:
h = 0.93m

## Slide 59
QUESTION
Consider a farm irrigation canal having the following dimensions: bottom width of 0.50 meters, total depth of 0.65 meters, side slopes of 2:1, depth of water of 0.50 meter, and channel slope of 1 meter per kilometer. Use n = 0.024. Determine the ff: cross-sectional area of the stream, wetted perimeter, hydraulic radius, and the discharge of the stream.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Answers: A = 0.75m2
P = 2.74m
R = 0.27m
Q = 0.41m3/s
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
A = (b + mh)h
A = [0.5 + 2(0.5)]0.5
A = 0.75m2
P = b + 2h
P = 0.5 + 2(0.5)
P = 2.74m
R = A/P
R = 0.75/2.74
R = 0.27m
Q = A
Q =
Q = 0.41m3/s

## Slide 60
QUESTION
A triangular channel section with a bottom angle 80 deg with channel gradient 0.0016 and n = 0.025, carries a discharge of 400 cfs, determine the normal depth and the velocity of flow.
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Answers: y = 9.68ft
V = 5.08fps
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Q = A
Q =
400cfs =
By shift solve:
h = y = 9.68ft
40°
40°
Slope, m = H/V
tan(40) = opp/adj = H/V
tan(40) = 0.84 = m
V
H
40°
Q = AV
V = Q/A
V = 400cfs/[0.84(9.682)]
V = 5.08fps

## Slide 61
QUESTION
Given a trapezoidal canal with cross-sectional area of 20 ft²; for best hydraulic section, what should be the depth of flow and the bottom width of the channel?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Answers: y = 3.4ft
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
A = 20ft2 = y2
y = 3.4ft
A = (b + mh)h
20 = [b + 0.577(.4)]3.4
b = 3.92ft
TAKE NOTE: for best trapezoidal section, m = 0.577

## Slide 62
QUESTION
The most hydraulically efficient trapezoidal channel section to carry a discharge of 5m3/s on a bed material with a roughness n of 0.02 and a bottom slope of 1 in 200 should have a bottom width of?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Answers: b = 1.27m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Q = A
Q =
5 =
By shift solve:
y = 1.1
A = (b + mh)h and for best trapezoidal section, A = y2
Therefore:
y2 = [b + 0.577(1.1)] x 1.1
b = 1.27m

## Slide 63
QUESTION
A concrete-lined trapezoidal canal is to carry a maximum discharge of 2.0 m3/s. The required head loss over a horizontal distance of 1 km is 2.0 m. The side slope is to be set at 1:1 and the permissible b/d ratio is 3. If the Manning’s roughness coefficient is 0.015, the design depth required is?
ATTRTC ABELE Review 2024
Irrigation and Drainage Engineering | Open Channel
Answers: y = 0.56m
ATTRC ABELE Review 2025
Irrigation and Drainage Engineering | Open Channel
Q = A
Q =
2 =
By shift solve:
y = 0.56m
Given: b/d = 3 or b/h = 3
Therefore, b can be expressed in terms of h. We can rewrite it as b = 3h.
Replacing all b values to 3h, we have

## Slide 64
THANK YOU
ABELE | 2025
ATTRTC - Iligan City